## Slide 1: Deck Equipment AGOR 27

## Slide 2
Deck Crane: TK70-70. 01 Deck aft
Portable Crane: TK4-30. 01 Deck fwd
Per Design Specification (J-1) Cranes Shall be capable of:
Loading and offloading vans and equipment weighing up to 20, 000 pounds 20’ beyond stbd side pier side.
Performing towing and coring operations with wire (including fiber optic) from the trawl/tow traction winch.
Deploying buoys and other heavy equipment weighing up to 10K lbs. up to 12’ over the Stbd. Side in sea state 4
Provided with a load hoist winch capable of providing hook drop at least 50’ below the base of the crane and at least 40’/min hook drop test
Hook speed of at least 40ft/min with a bare drum and at least 60ft/min with a full drum

## Slide 3: CTD Handling System
CTD-LARS
Stbd.Side Handling System

## Slide 4: Stern Frame
Allied A-30 (243 x 324”)
Per Design Specification (J-1) Stern Frame Shall be capable of:
Dynamic Safe Working Load of 30,000 Lbs through full range of motions.
Capable of withstanding the 46 CFR 189.35 breaking strength requirements for a wire with a breaking strength of 120,000 in fully extended position
Rotation Period of no more than 35 Seconds from stop to stop
Height from block attachment points to the deck of 27 feet and a clear width between the legs of at least 15 feet above the deck
Minimum 12 foot inboard and outboard reach
Maintenance position rotates top of frame within a safe working height above the main deck (4’9”) to change blocks and cable fairleads.

## Slide 5: Hydrographic Winches (2)
Markey CAST -6-125
Electric Motor Driven
Rated at 24,000 Lbs
A pushbutton operator interface enables the level wind to electronically adjust to any diameter wire, cable or soft-line
The output sheave of the fairlead is mounted in a flagging block which sweeps 360 degrees. This unique design eliminates the need for deck hands to carry and rig intermediate blocks or fairleads, resulting in less time spent rigging, more time for sampling, which reduces overall operational time and expense.
Per Design Specification (J-1) Stern Frame Shall be capable of:
Capable of a line pull test of at least 5,000 pounds with a full drum and at least 11,100 pounds with a bare drum
Capable of variable speeds up to at least 1.5 meters/sec under full load
Capable of handling cable sizes and lengths up to and including 10,000 meters of 0.393 inch EOM cable.
One winch provided with lebus shells sized for .322” EM cable the other with 3/8”, 3x19 torque balanced wire rope

## Slide 6: Traction Winch
Markey DETW-9-11
26,500 Lbs @ 0-205 Ft/Min
Electric Motor Driven
AC Variable Frequency Drive System and electric motors giving precise control.
Lebus-grooved drum shells.
Per Design Specification (J-1) Traction Winch Shall be capable of:
Full load line pull of at least 25,000 pounds and continuous speed control to 0.1 meters/min throughout the speed range
Handling 12,000 meters of 9/19 3x19 wire and 10,000 meters of 0.680 EM cable
Winch and sheave shall be capable of handling 0.681 inch fiber optic cable
Cooling of stowage winch drums to reduce heat build up when transmitting high power levels through the cable to ROV’s

## Slide 7: Deck Working Space Aft clear deck space – 1873 ft2 Total clear deck space – 2557 ft2