## Slide 1
Nutrient Group
To ensure general acceptance of time series nutrient data, the Quality Assurance/Quality Control procedures MUST be carefully documented in the metadata/reference publications. This includes analysis of appropriate Reference Materials/External Performance Evaluations to ensure comparability and consistency.

## Slide 2
Nutrient Group
Macronutrient analytical methods
Best – Autoanalyzer + Low Level Nutr. Methods (where appropriate)
Good – Autoanalyzer
Acceptable – Manual analyses (emerging UV methods can reduce need for Cd columns)
Are methods intercomparable? Lot’s of subtleties (linear/non-linear cal. curves, blanks…) – requires Reference Materials to ensure method comparability

## Slide 3
Nutrient Group
Standards/Reference Materials
Primary standards & low nutrient seawater – OSIL
Seawater reference solution - Kanso
Performance evaluation samples – OSIL, Quasimeme
There needs to be a community evaluation of “standards” to assess best practice/performance of stds.
SCOR Working Group on standards (not successful, needs encouragement)

## Slide 4
Emerging technology/chemistry
Ammonium analyses – often ignored, but importance underestimated
  OPA
  Conductivity
Phosphate – malachite green
UV nitrate – can be used in
Enzymatic nitrate reduction – green chemistry

## Slide 5
Nutrient Group
Sampling/Preservation
Immediate analysis ideal, but freezing is a reality for many time series
  Limited storage time for phosphate
  Si polymerization may require two continuous flow analyzer runs
Filter/not filter – depends on environment
  Filter blanks dictate filter type – must test

## Slide 6
Iron – historically not in time series because it was hard. Not the case anymore.
SAFe & Geotraces Reference Materials available.
Many shipboard automated analytical methods now available (FIA-CL, FIA-spectrophotometry, CSV). Most directly comparable.
Modified rosette (external closure bottles, powder coat metal) works.

## Slide 7
Nutrient Group
Macronutrient nomenclature
Nitrate (is it nitrate or nitrate + nitrite?),
Dissolved phosphate or Soluble Reactive Phosphate.