## Slide 1: Applications of Satellite Gravity Measurements to Studying Sea Level Change
R. Steven Nerem
University of Colorado
Department of Aerospace Engineering Sciences
Colorado Center for Astrodynamics Research
Cooperative Institute for Research in Environmental Sciences
“If there is magic on this planet, it is contained in water.” Loren Eiseley (American essayist, philosopher, and literary naturalist, 1907-1977)

## Slide 2: What Causes Sea Level to Change?

## Slide 3: Causes of Sea Level Change
Thermal Expansion (~ 1 meter potential)
Water Exchange with Continents (potential)
  Greenland Ice (7 meters)
  Antarctic Ice (60 meters)
  Mountain Glaciers (0.7 meter)
  Terrestrial Water Storage Variations (< 0.5 meter)

## Slide 4: Measurement Systems
GRAVITY
Argo

## Slide 5: Reconstructed Tide Gauge Sea Level
[Church and White, 2011]
Average Rate (1950-2010): ~1.8 mm/year

## Slide 6: Satellite Altimetry
Trend = 3.1 mm/year

## Slide 7: GRACE Gravity Recovery and Climate Experiment

## Slide 8: Where is the Water?

## Slide 9: Satellite Laser Ranging (SLR)

## Slide 10: Dedicated Satellite Gravity Missions
Geodetic Satellite Laser Ranging
  Starlette (1975-present)
  LAGEOS (1976-present)
  LAGEOS II (1992-present)
Dedicated Satellite Gravity Missions
  CHAMP (DLR, 2000, 5 years, GPS/accelerometer)
  GRACE (NASA & DLR, 2002, 5 years, satellite-to-satellite microwave link/GPS/Accelerometer)
  GOCE (ESA, 1 year, gradiometer): static field main goal
Future/Proposed
  GRACE Follow-On (NASA, 5-10 year mission, 2016?)
    main goal is an extended time variable field

## Slide 11: Starlette
Passive geodetic satellite
  Launch date: 6 Feb 1975
  Weight: 47.25 kg
  Diameter: 36 cm
  Perigee Height: 812.19 km
  Apogee Height: 1114.8 km
  Eccentricity: 0.0206
  Inclination: 49.83 degree
  Semi-major axis: 7331 km
  Contains 60 laser corner reflectors

## Slide 12: Modeling the Earth’s Gravity Field: Spherical Harmonics
Where  is latitude,  is longitude, a is the mean radius of the Earth, and Clm and Slm are dimensionless Stokes coefficients.
The Earth’s geoid can be expanded as a series of normalized associated Legendre functions:

## Slide 13: Early gravity model history
1958-1961: Tracking of Sputnik 2, Explorer 1, Vanguard 1
  Zonal coefficients estimated (C20 , C30 , C40 )
  Degree 2 sectorial (C22,S22) and tesseral coefficients
    Found adding camera observations to tracking
1966: Smithsonian Astrophysical Observatory
  Degree and order 8
  Doppler tracking and Baker-Nunn camera observations
1970: Degree and order 16
  Addition of satellite laser ranging
1977: Solutions approach limits of ground-based tracking
  Altimetry missions GEOS-3(1975) and Seasat (1978) allow for ranging and mean sea surface measurements to be included

## Slide 14: Major global geopotential models
Standard Earth Models (SE) 1966-1977
  Smithsonian Astronomical Observatory
Goddard Earth Models (GEM)
  Goddard Space Flight Center
GRIM (1965–present)
  Geodetic Research Institute in Munich (now GFZ)
  Groupe de Recherches de Geodesie Spatiale (France)
Ohio State University (OSU91)
University of Texas at Austin (TEG 1–4)
Joint Geopotential Model (JGM 1–3)
Earth Gravitational Model 1996 (EGM96)
  (70x70 and 360x360)

## Slide 15: EGM96 30’ mean gravity anomalies

## Slide 16: EGM96 geoid heights

## Slide 17: EGM96 geoid height errors

## Slide 18: Geoid error improvements

## Slide 19: Orbit error improvements
From SLR fit residuals to TOPEX/Poseidon.

## Slide 20: Earth’s Oblateness (J2)

## Slide 21: J2 Variations from Satellite Laser Ranging
Cheng and Ries [2010]

## Slide 23: GRACE Payload
Micro-wave Tracking:
    Separation distance 220 km (Los Angeles to San Diego)
    Dual One-Way Tracking System (K/Ka band)
    Refinements to Original GRAVSAT/GRM concept from 1980
      Antenna: NASA DSN heritage
JPL Turbo-Rogue Receiver:
    Digital Signal Processing for SST link
    GPS Tracking for Orbit Determination
    Proven, Geodetic Quality Space Receiver
Ultra-Stable Oscillator:
    Frequency reference
    JHU/APL Mars Observer heritage
Accelerometer:
    For modeling of non-gravitational accelerations
    Obviates need for expensive drag compensation mechanisms
    Refinement of STAR accelerometer, from CHAMP heritage

## Slide 24: The GRACE Satellites

## Slide 25: Accelerometer Concept
Drag
Solar Radiation
Pressure

## Slide 26: Future Missions: Drag Free?
Drag
Solar Radiation
Pressure

## Slide 27: Surface Mass Density
Changes in the gravity coefficients used to describe the geoid height can be expressed in terms of change in surface mass density:
Where kl is the load love number of degree l, and which represents the effect of the Earth’s elastic response to a change in surface load.

## Slide 28: GRACE Errors
Estimates of the square root of the contribution to the variance of the inferred surface mass anomaly due to GRACE satellite measurement error.
GRACE measurement error increases for high-degree, short-wavelength gravity coefficients.
Correlation between these errors results in longitudinal stripes in mapped anomaly fields.
mm
GRACE Unsmoothed mass anomaly

## Slide 29: Gaussian smoothing of GRACE mass anomaly maps
Unsmoothed
250 km halfwidth
c. 500 km halfwidth
d. 750 km halfwidth
(Swenson and Wahr, 2006)

## Slide 30: Smoothed Mass Anomalies
a = Earth radius r = Gaussian half-width
Using the following recursive relationship to determine averaging coefficients Wl:
where
A smoothed map of surface mass anomaly can be derived using the GRACE coefficients as:

## Slide 31: Weighting Function
Wahr et al. (1998)

## Slide 32: Weighting Function
Wahr et al. (1998)

## Slide 33: “Destriping” of GRACE mass anomaly maps
No filtering
(Swenson and Wahr, 2006)
Correlated-error filtering
No smoothing
500-km half-width Gaussian

## Slide 34: Simulations Using Two Pairs of GRACE Satellites
Two Pairs
One Pair
Truth
One Pair, destriped & 300km smooth
[Wiese, 2011]

## Slide 35: Determining mass variations in kernel region
While the Legendre functions are used in computing the Stokes coefficients for the averaging kernel and the mass anomaly, they are not needed to determine the surface mass density in the kernel region. The average surface mass density change is found as:
Where the Stokes coefficients for the averaging kernel are found:

## Slide 36: Summary: Recovery of Surface Mass
Where:
DN = geoid height change
Ds = surface mass density
Mass anomalies can be separated horizontally, but not vertically.

## Slide 37: GRACE Geoid Errors
[Tapley et al., 2004]
EGM-96
GRACE

## Slide 38: GRACE Surface Water Anomalies

## Slide 39: GRACE Water Thickness Changes
[Jacob et al., 2012]

## Slide 40: GRACE Water Thickness Changes – GIA removed
[Jacob et al., 2012]

## Slide 41: Global Ocean Averaging Kernel

## Slide 42: Global Ocean Mass from GRACE
Updated from Chambers et al. [2004]

## Slide 43: Global Ocean Mass from GRACE
Updated from Chambers et al. [2004]

## Slide 44: Greenland Ice Mass Changes from GRACE
Rate of Ice mass change:
All Greenland: -239 Gton/yr
South Greenland: -162 Gton/yr
North Greenland: -77 Gton/yr
April, 2002 – June, 2010
-239 Gton/yr = 0.66 mm/yr sea level rise
(1 Gton = 1 km3 of water)
[Wahr, 2010]

## Slide 45: Greenland Ice Mass Changes from GRACE

## Slide 46
GRACE-observed mass changes in the Arctic

## Slide 47: Antarctica Ice Mass Variations from GRACE
Rate of ice mass change:
All Antarctica: -143 Gton/yr
West Antarctica: -155 Gton/yr
East Antarctica: +15 Gton/yr
Uncertainty of GIA correction:
All Antarctica: ± 80 Gton/yr
West Antarctica: ± 20 Gton/yr
East Antarctica: ± 55 Gton/yr
-143 Gton/yr = 0.40 mm/yr sea level rise
April, 2002 – June, 2010
[Wahr, 2010]

## Slide 48: Polar Ice Mass Loss from GRACE
[Velicogna, 2011]

## Slide 49: Are Greenland and Antarctica Accelerating?
[Rignot et al., 2011]
Total GMSL
Contribution
2050: 15 cm
2100: 56 cm

## Slide 50: Mascons Used in GRACE Analysis
[Jacob et al., 2012]

## Slide 51: Ice Mass Changes from GRACE
[Jacob et al., 2012]

## Slide 52: Ice Mass Changes from GRACE
[Jacob et al., 2012]

## Slide 53: GRACE Water Thickness Changes in Asia
[Jacob et al., 2012]

## Slide 54: Current Sea Level Budget (~Altimeter Era)
Thermal Expansion: ~ 1.1 mm/year
Mountain Glaciers: ~ 1.2 mm/year
Greenland Ice Melt: ~ 0.6 mm/year
Antarctic Ice Melt: ~ 0.4 mm/year
Land Water Storage: ?
Total: ~ 3.3 mm/year
+
+
+
=

## Slide 55: Current Sea Level Budget (~Altimeter Era)
Thermal Expansion: ~ 0.8 mm/year
Mountain Glaciers: ~ 0.4 mm/year
Greenland Ice Melt: ~ 0.7 mm/year
Antarctic Ice Melt: ~ 0.4 mm/year
Land Water Storage: ?
Total: ~ 2.3 mm/year
+
+
+
=

## Slide 56: Sea Level and Ice Sheets
Higher sea level
due to ice sheet

## Slide 57: Sea Level Fingerprints via GRACE Mass Change
[Riva et al., 2010]

## Slide 58: J2 Variations from Satellite Laser Ranging
Cheng and Ries [2010]

## Slide 59: J2 Variations from Satellite Laser Ranging

## Slide 60: GRACE Observations of Polar Ice Mass Loss
225 Gtons/year
156 Gtons/year

## Slide 61: GIA-Corrected J2 Variations

## Slide 62: Satellite Altimetry
Trend = 3.1 mm/year

## Slide 63: Detrended GMSL versus MEI

## Slide 64: The Two Decades of the Altimeter Era

## Slide 65: Spatial Variations in Sea Level Rise 1993-2011

## Slide 66: Western Pacific Sea Level Change
Merrifield (2010)

## Slide 67: Closing the Sea Level Budget
+
=
Total Sea Level Rise
Argo
Jason
GRACE
(roughly)
Addition of Freshwater
Addition of Heat

## Slide 68: Global Mean Sea Level Changes
[Boening et al., 2012]

## Slide 69: GRACE Water Mass Change (MAM 2011 – JFM 2010)
[Boening et al., 2012]

## Slide 70: Major Land Contributions to Ocean Mass
[Boening et al., 2012]

## Slide 71: Sum of Major Land Contributions
[Boening et al., 2012]

## Slide 72: What Will Happen in the Future?
Coupled climate models
IPCC, 2007
Empirical projections
Rahmstorf, 2007

## Slide 73: It’s all about the water!

## Slide 74
Thanks!

## Slide 75: Predicted Regional Patterns of Sea Level Change
[Bamber, 2009]

## Slide 76: Total Sea Level and Ocean Mass

## Slide 77: Acceleration of Mountain Glaciers
[Dyurgerov and Meier, 2005]
1961-1993: 0.5 mm/year
1993-2003: 0.9 mm/year

## Slide 78: Sea Level Contributions
GRACE Ocean Mass
Ocean Measurements (Argo)
Thermosteric sea level
Total Sea Level – Satellite Altimetry

## Slide 79: GRACE Secular Trends (2002-2011)
[Wahr, 2011]
GIA Model
Removed

## Slide 80: Glacial Isostatic Adjustment (GIA)
[James et al., 2005]

## Slide 81: Glacial Isostatic Adjustment (GIA)
-7.0 -2.0 -1.5 -1.0 -0.5 0 0.5 1.0 1.5 2.0 25.0
Present-Day Radial Deformation (mm/year)
[Milne, 2005]

## Slide 82: Is Antarctic Ice Mass Loss Holding Steady?
[Wahr, 2010]