## Slide 1
December 2006
Charles W. Holland,
The Pennsylvania State University, USA
Thoughts on
Sonar Performance Prediction Uncertainty
Due to the Ocean Environment
(esp Seabed in Shallow Water)

## Slide 2: Outline
Comments on uncertainty
Seabed Characteristics in East China Sea

## Slide 3: Problem Statement
Uncertainties in acoustic performance prediction
lead to
inability of the Fleet to make judicious decisions about tactics & employment of resources.

## Slide 4: Uncertainty due to Ocean Environment
Uncertainties (U) are due to:
  Sensitivity (S) of performance to environment
  Variability (V) of environment
  environment Measurement (M) capability

## Slide 5: Uncertainty due to Ocean Environment
Uncertainties (U) due to:
  Sensitivity (S) to env.
  Variability (V) of env.
  env. Measurement (M) capability

## Slide 6: (Simplified) Assessment of Measurement Capability (M)
Scale 1-10; low-high | Seabed | Water Column
Measurements | 6 | 10
uncertainties | 4 | 10
Regional Predictions | 2 | 7
uncertainties | 1 | 5
Passive
 | Seabed | Water Column
Measurements | 4 | 10
uncertainties | 2 | 10
Regional Predictions | 1 | 7
uncertainties | 0 | 5
Active

## Slide 7: Uncertainty due to Ocean Environment
Uncertainties (U) due to:
  Sensitivity (S) to env.
  Variability (V) of env.
  env. Measurement (M) capability

## Slide 8: Sensitivity (passive)
Propagation: important!! to distinguish between
  Narrowband vs Broadband (coherent vs incoherent)
  Fixed-fixed vs range variable geometry
By and large our goal is to predict uncertainties associated with incoherent propagation

## Slide 9: Sensitivity to Seabed Properties
In a Pekeris Waveguide, can write intensity as,
Io source intensity @ 1m
H water depth
r range
c critical angle
R int. reflection coefficient
N number of bounces
= r tan/2H
At 25 km N(10)~20,
  so for a single mode at 10
  an error of 0.5 dB in R,
  leads to 10 dB error in TL = -10 log(I/Io)
So, Sensitivity S is high (i.e., small errors in seabed properties (and R) lead to large errors in TL and reverb)

## Slide 10: Variability of Seabed Properties
In some situations we can approximate ,
Variability (V)
  1.1<<2.1 , 1.1<<2.5 g/cc
  1470<c<1900, 1470<c<5500 m/s
  0.005<<3 dB/m/kHz
and in a VERY simplistic way we can approximate ,

## Slide 11: Uncertainty due to Ocean Environment
Uncertainties (U) due to:
  Sensitivity (S) to env.
  Variability (V) of env.
  env. Measurement (M) capability
M is low
V is high (e.g., attenuation is almost 3 orders magnitude)
S is high (small errors are greatly magnified with range)
Bottom Line, we expect typical uncertainties in seabed properties to lead to large uncertainties in sonar performance prediction

## Slide 12: Comparison of Measured TL with Fleet Models/Databases (Ferla and Jensen, 2002)
Objectives of study
  How good are current databases used by Fleet?
  Where are the biggest problems?

## Slide 13: Comparison of Measured TL with Fleet Models/Databases (Ferla and Jensen, 2002)
10 dB
Straits of Sicily
10 dB
Norweg. Sea 180m
Key results:
  TL predictions show biases of order tens of dB with respect to measurements.
  Most of these errors were traced to limitations in present generation seabed databases

## Slide 14: Summary Thoughts on Uncertainty
If we ignore coupling between water column and seabed, we can think (generally) of two distinct impacts of env. uncertainty (sensitivity/variability/measurement capability) :
  Effect of seabed uncertainty on sonar performance primarily induces (range-dependent) bias errors
  Effect of water column uncertainty on sonar performance primarily induces fluctuation errors
Therefore
  Addressing sonar performance uncertainty due only to water column variability, will give Fleet totally inadequate answer (fluctuations on top of large bias errors)
  Addressing sonar performance uncertainty due only to seabed variability, will give Fleet totally inadequate answer (correct mean without fluctuations)

## Slide 15: Seabed Characteristics in ECS
Multi-national 2001 ECS experiment, num. papers incl. IEEE special issue, NB: the science issues at the time drove the site selection towards simplicity, i.e., there was a concerted effort to minimize the impact of variable oceanography, variable bathymetry, and complex geoacoustic range dependence.
However, in the FY09 experiment, it is likely that more realistic seabed environments must be/will be encountered. For example, propagation near and across the shelf break means not only more complex oceanography but also substantially more complex variability in the geoacoustic properties.

## Slide 16
Example
(of complexity/variability)

## Slide 17: ECS Seabed
Mud volcanoes discovered near shelf break; believed common on outer shelf and upper western slope of Okinawa Trough (Yin et al, Mar Geo, 194, 2003)
  5-40 m in height and with radii of ~20-600 m.
  pockmarks up to 40m in depth and 300m in diameter
2001 Acs exp.
NB: in recent surveys NAVOCEANO has also observed MVs in this area

## Slide 18: What Are Mud Volcanoes?
Mud volcanoes are seabed (or sub-seabed) features that form due to the rise of fluidized sediments and/or gas along a fault or on top of a seafloor-piercing shale diapir.
They may occur in sedimentary areas with hydrocarbon generation at depth, originate from thick clay beds, usually erupt along fault lines, and often bubble gas (mostly methane), and sometimes oil.
That there is methane in ECS sediments is implicit in the high concentrations of methane in ECS seawater (Zhang et al., JGR, 2004).

## Slide 19: Are Mud Volcanoes Important for ASW?
The geoacoustic properties of these features are not yet well understood, and are expected to be time varying, amount and size distribution of interstitial gas bubbles in the sediments (or water column) depends upon the oceanography as well as local tectonics, microseisms, etc…
Passive: range/time dependent propagation effects
~2 m
Active: passive effects plus clutter (increase of false alarm rate)
Carbonate precipitate on flanks

## Slide 20: Impact of Mud Volcanoes on ASW
Recent measurements on mud volcanoes in Straits of Sicily (of a similar scale) show:
  target strengths of 6-12 dB from 160-3600 Hz (Holland et al., JASA, 2006)
  Heavy tailed reverberation (i.e., non-Rayleigh) leading to increased false alarm rate
  Modeling shows that tracking algorithms may easily be confused by a MV cluster along fault lines/crossings
Bottom line: MVs which exist on scales of a target, are expected to significantly impact active sonar performance.

## Slide 21: Impact of Mud Volcanoes on Active ASW
1400 Hz
Mud Vol.
Directional reverberation on towed array; MV is on outer shelf, 20 km from source-rec
Prakla HF aperture: frequency dependence dominated by beamwidth

## Slide 22: ECS Seabed Summary
1) What we know
  • ONR 2001 experiment mid to outer shelf, ~30 km x 30 km
  literature survey (G&G) shows many references to inner shelf, fewer to middle and outer shelf
  presence of mud volcanoes and gassy sediments near outer shelf suggest performance will be complicated there
  Other data sources:
    NAVOCEANO has data - updated database have included velocity dispersion and non-linear attenuation vs frequency
    NRL Stennis (D. Lavoie) late 90’s ASW/MCM maps
    Taiwanese core database and chirp lines, NGDC, etc…
2) What we don’t know
  • key issue is lack of regional models; spatial variability of geoacoustic properties;
  • methods for quantifying and predicting geoacoustic uncertainty