## Slide 1: RV ARMSTRONG, AGOR 27
November 2013 Institution update

## Slide 2: RV ARMSTRONG, AGOR 27
Oceans Class Characteristics
Length OVA = 238’-0” Beam = 50’-0”
Design Speed = 12.0 kts Endurance = 40 days
Crew Size = 20 Science Party Size = 24

## Slide 3: RV ARMSTRONG AGOR 27 Delivery date: October 2014 Science verification cruise(s) ~January 2015 – ~ April 2015
Science Mission Equipment
Lab Layouts
Deck handling systems (winches and crane)
A Frame
Deck layouts

## Slide 4: AGOR 27 Science Equipment List
Funded In Vessel Construction Budget
Kongsberg EM122 Multibeam
SeaBird TSG
Knudsen 3260 Sub Bottom Profiler
Massa TR109 3.5 kHz transducer Array
12 kHz transducer Array
POS/MV Precision GPS
Satellite Communication System
38 kHz RDI Ocean Surveyor ADCP
Acoustic Monitoring System
Science Seawater Distribution System

## Slide 5: AGOR 27 Science Equipment List
DURIP (Navy) Funded Equipment
Kongsberg EM710 Multibeam
Kongsberg Sonar Synchronization System
75 kHz RDI Ocean Surveyor ADCP
300 kHz RDI Workhorse Mariner ADCP
Kongsberg HiPAP Gantry with Sonardyne USBL
Kongsberg EK60 Mid-Water Echo Sounder
RADAR Wave Height Measurement System
OTHER (NSF?) Funded Equipment
AUV High Bandwidth Communications
Plotters

## Slide 6: 19 inch transducer wells avail for science
EM122
EM122
Knudsen 3260
EM710
75 kHz ADCP
38 kHz ADCP
300 kHz ADCP
12 kHz Transducer
USBL stem
Transducer Room Layout
EM710

## Slide 7: Complete Lab Layout

## Slide 8: Wet Lab & Staging Bay

## Slide 9: Main Lab

## Slide 10: Computer Lab

## Slide 11: Science Storeroom

## Slide 12: Deck Equipment AGOR 27

## Slide 13: Hydrographic Winches (2)
Markey CAST -6-125
Electric Motor Driven
Rated at 24,000 Lbs
A pushbutton operator interface enables the level wind to electronically adjust to any diameter wire, cable or soft-line
The output sheave of the fairlead is mounted in a flagging block which sweeps 360 degrees. This unique design eliminates the need for deck hands to carry and rig intermediate blocks or fairleads, resulting in less time spent rigging, more time for sampling, which reduces overall operational time and expense.
Per Design Specification (J-1) Stern Frame Shall be capable of:
Capable of a line pull test of at least 5,000 pounds with a full drum and at least 11,100 pounds with a bare drum
Capable of variable speeds up to at least 1.5 meters/sec under full load
Capable of handling cable sizes and lengths up to and including 10,000 meters of 0.393 inch EOM cable.
One winch provided with lebus shells sized for .322” EM cable the other with 3/8”, 3x19 torque balanced wire rope

## Slide 14: Traction Winch
Markey DETW-9-11
26,500 Lbs @ 0-205 Ft/Min
Electric Motor Driven
AC Variable Frequency Drive System and electric motors giving precise control.
Lebus-grooved drum shells.
Per Design Specification (J-1) Traction Winch Shall be capable of:
Full load line pull of at least 25,000 pounds and continuous speed control to 0.1 meters/min throughout the speed range
Handling 12,000 meters of 9/16” 3x19 wire and 10,000 meters of 0.680 EM cable
Winch and sheave shall be capable of handling 0.681 inch fiber optic cable
Cooling of stowage winch drums to reduce heat build up when transmitting high power levels through the cable to ROV’s

## Slide 15: Deck Working Space Aft clear deck space – 1873 ft2 Total clear deck space – 2557 ft2

## Slide 16: Stern Frame
Allied A-30 (243 x 324”)
Per Design Specification (J-1) Stern Frame Shall be capable of:
Dynamic Safe Working Load of 30,000 Lbs through full range of motions.
Capable of withstanding the 46 CFR 189.35 breaking strength requirements for a wire with a breaking strength of 120,000 in fully extended position
Rotation Period of no more than 35 Seconds from stop to stop
Height from block attachment points to the deck of 27 feet and a clear width between the legs of at least 15 feet above the deck
Minimum 12 foot inboard and outboard reach
Maintenance position rotates top of frame within a safe working height above the main deck (4’9”) to change blocks and cable fairleads.

## Slide 17
Deck Crane: TK70-70. 01 Deck aft
Per Design Specification (J-1) Cranes Shall be capable of:
Loading and offloading vans and equipment weighing up to 20, 000 pounds 20’ beyond stbd side pier side.
Performing towing and coring operations with wire (including fiber optic) from the trawl/tow traction winch.
Deploying buoys and other heavy equipment weighing up to 10K lbs. up to 12’ over the Stbd. Side in sea state 4
Provided with a load hoist winch capable of providing hook drop at least 50’ below the base of the crane and at least 40’/min hook drop test
Hook speed of at least 40ft/min with a bare drum and at least 60ft/min with a full drum

## Slide 18: RV ARMSTRONG, AGOR 27
Main Deck (working deck)

## Slide 19: Working Deck Examples with 5 lab vans, portable winch and CTD operation

## Slide 20: RV Armstrong with ROV Jason example layout

## Slide 21: RV ARMSTRONG, AGOR 27
Summer 2013

## Slide 22: RV ARMSTRONG, fall 2013

## Slide 23: RV Armstrong starboard side fall 2013